## Slide 1: uProcesoru sistēmu projektēšana un skaņošana
Piezīmes
3 lekcija – Hardware Support. Processor Architectures, Buses, I/O

## Slide 2: A Purpose of a Lection
Discuss the embedded hardware Linux supports.
Will cover the processor architectures Linux supports commonly used in embedded systems.
Will cover the various hardware components involved, such as buses, I/O, storage, general-purpose networking, industrial-grade networking, and system monitoring.

## Slide 3: Processor Architectures
Not all are actually used in embedded configurations.
We will cover 8 architectures that are used in embedded Linux systems (in alphabetical order): ARM, AVR32, Intel x86, M32R, MIPS, Motorola 68000, PowerPC.

## Slide 4: ARM
There is no central producer of ARM chips.
All ARM processors share the same ARM instruction set.
The assembly language and resulting binary codes are identical for all ARM processors meeting a certain revision of the architecture.
For example, the ARMv4T introduced a condensed version of the instruction set (“Thumb”) that aims to use less memory for instruction storage, while maintaining an adequate level of performance.
There are also ARM processors with enhanced DSP performance (“E”), Java bytecode support (“J”), virtualization capabilities, and a growing number of other flags.
The ARM architecture is very popular in many fields of application, from cell phones and PDAs to networking equipment, and there are hundreds of vendors providing products and services around it.

## Slide 5: AVR32
It is a 32-bit microprocessor architecture designed by the Atmel corporation, which also produces the AVR 8-bit microcontroller devices used in deeply embedded situations.
AVR32 comprises several subarchitectures and can additionally support the usual DSP and Java acceleration instructions.
AVR32 provides for several modes of CPU operation; both fixed width 16-bit instructions and “extended” 32-bit instructions are supported.
16-bit width instructions are similar in purpose to the ARM Thumb.
The initial port of Linux to AVR32 was announced in a posting to the Linux Kernel Mailing List in early 2006.

## Slide 6: Intel x86
Although x86 is the most popular and most publicized platform to run Linux, it represents a small fraction of the traditional embedded systems market.
In most cases, designers prefer ARM, MIPS, and PowerPC processors to i386.
i386 remains the most widely used and tested Linux platform.
The largest base of software available for Linux.
The kernel itself was in fact written for the i386 first.
most, if not all, i386 embedded systems are very similar, or identical to the workstation and server in terms of functionality and programmability.
The kernel makes little or no difference between the various x86 CPUs and related boards.
The i386-based PC architecture is the most widely documented architecture around.

## Slide 7: M32R
M32R is another recent (2003) 32-bit microprocessor architecture, designed by Renesas Technology and implemented both in silicon and as an FPGA synthesized soft-logic core.
M32R actually implements a full MMU and can therefore run a stock Linux kernel without using uClinux’s user space utilities.
M32R has been used in a variety of applications, ranging from consumer electronics devices such as PDAs, cameras, and the like to engine control units.
The Linux port supports nearly a dozen platforms based upon M32R.

## Slide 8: MIPS
MIPS is famed for once having been the basis of the workstations and servers sold by SGI and of gaming consoles such as Nintendo’s 64-bit (N64) system and the Sony Playstations 1 and 2.
MIPS Technologies Inc., licenses CPU cores to third parties much like ARM.
Unlike ARM, however, there are in fact many instruction set implementations.
The initial port of Linux to MIPS was mainly done to support MIPS-based workstations.
The actual type of MIPS chip on the board is much less important than the type of environment in which it is placed.
Support for Linux on MIPS is more limited than for other architectures such as the Intel x86 or the PowerPC.
Few of the main distributions have actually been ported to MIPS.

## Slide 9: Motorola 68000
The Motorola 68000 family is known in Linux jargon as m68k.
m68k came in second only to the Intel x86 as a popular 1980s architecture.
Recently, though, interest has drifted away from the m68k to newer architectures, such as ARM, MIPS, SH, and PowerPC, for embedded systems design.
From time to time new boards appear that are based upon this venerable architecture.
Linux supports many systems based on m68k, starting with the mainstream and workstation systems.

## Slide 10: PowerPC
PowerPC (PPC) architecture was the result of a collaboration between Apple, IBM, and Motorola (now Freescale)—the “AIM alliance.”
PowerPC is mostly known for its original use in Apple’s Macs, but there are other PowerPC-based workstations from IBM and other vendors, as well as many PowerPC-based embedded systems.
Along with i386 and ARM, the PowerPC is the best supported architecture in Linux.
It is clear that PowerPC Linux has benefited from some big players being behind it, it has also been successful because of a small but very dedicated number of core PowerPC developers.
A great number of applications that run on the Intel x86 are available for PowerPC.

## Slide 11: Buses and Interfaces
The buses and interfaces are the fabric that connects the CPU to the peripherals on the system.
Each bus and interface has its own intricacies, and the level of support Linux provides.
A rundown follows of some of the many different buses and interfaces found in typical embedded systems, and the level of support Linux provides them.

## Slide 12: PCI/PCI-X/PCIe
The Peripheral Component Interconnect (PCI) bus, managed by the PCI Special Interest Group (PCI-SIG), is the most popular bus currently available. Designed as a replacement for the legacy Intel PC ISA bus, PCI is now available in two forms:
  120 (32-bit PCI) I/O lines
  84 (64-bit PCI-X) I/O lines
  PCI Express (commonly called PCIe or PCI-E).
Linux support is very good.
PCI requires software support in order for it to be used by device drivers:
The first part of this support is required to initialize and configure the PCI devices upon bootup (called PCI enumeration).
On PC systems, this is traditionally done by the BIOS, and if the BIOS has carried out the initialization, the kernel will browse the BIOS’s table to retrieve the PCI information.
The kernel is capable of carrying out the initialization and configuration itself.
In both cases, the kernel provides an API to device drivers.

## Slide 13: ExpressCard (Replaces PCMCIA’s PC Card)
Modern laptop and embedded devices replace the legacy PC Card first standardized by PCMCIA with a higher speed standard known as ExpressCard.
ExpressCard is intended to allow for easy addition of internal peripheral devices to embedded devices in situations where, perhaps, using another bus such as USB is not desirable or practical.
This is true for laptops, where a given device should be added permanently.
ExpressCard simply provides both PCI-Express and USB 2.0 through a convenient interface card format.
ExpressCard already has good Linux support, and a growing number of systems are beginning to deploy it.

## Slide 14: PC/104, PC/104-Plus, PCI-104, and PCI/104-Express
Although many embedded devices today make use of regular desktop and server buses such as PCI and PCI Express, certain applications demand that they be hosted in a more robust form.
PC/104 defines a form factor for stackable computer processor boards.
There are several forms of PC/104 depending upon whether a PCI or PCI-Express bus is provided.
Devices built using the PC/104 form factor are supported by Linux.

## Slide 15: CompactPCI/CompactPCIe
The CompactPCI specification provides an open and versatile platform for high-performance, high-availability applications.
Technically, the CompactPCI bus is electrically identical to the PCI bus.
Instead of using slot connections, pin connectors are used to connect the vertically loaded CompactPCI boards to the CompactPCI backplane.
The CompactPCI specification allows for the implementation of the hot swap specification.

## Slide 16: CompactPCI/CompactPCIe
There are three levels of hot swapping:
  Basic hot swap: involves console intervention by the system operator. When a new card is inserted, she must manually inform the OS (power up, config., inform software). To remove a card, she must tell the OS that the board is about to be removed.
  Full hot swap: does not require console intervention by the operator. The operator flips a microswitch attached to the card injector/ejector to notify the OS. The OS performs the necessary operations to isolate the board and to shut down it. The OS lights an LED to notify the operator that the board can now be removed.
  High availability: CompactPCI boards are under complete software control. If a board fails, for example, the controller can shut it down and power up a duplicate board.

## Slide 17: SCSI/iSCSI
SCSI is a both a general software interface and a set of electrical specifications that can be used to connect various hardware peripherals.
Only a small segment of embedded systems (typically high-end embedded systems, such as NAS) ever use SCSI devicesnect various hardware peripherals.
Usually implement iSCSI, where the SCSI protocol is used over regular TCP/IP.
Linux support for SCSI is extensive and well maintained, while iSCSI support varies depending upon whether you wish to implement an initiator (client), target (device), or both.

## Slide 18: USB
Mostly a mainstream device-oriented bus.
USB is increasingly appearing in hardware used in embedded systems.
USB devices are connected in a tree-like fashion.
The root is called the root hub and is usually the main board to which all USB devices and nonroot hubs are connected.
Support within Linux for USB devices is very good.
The main component of Linux’s USB support is provided by the USB stack in the kernel.
The kernel also includes drivers for the USB devices supported by Linux.

## Slide 19: IEEE1394 (FireWire)
FireWire is a trademark owned by Apple. They later submitted their work to the IEEE - became IEEE standard 1394.
IEEE1394 enables devices to be connected using simple and inexpensive hardware interfaces.
In contrast to USB, IEEE1394 connections do not require a root node.
Linux’s support for IEEE1394 used to be buggy and was certainly incomplete in comparison with other operating systems.
IEEE1394 support was completely rewritten in the 2.6 series Linux kernel and is now widely considered to be very good.

## Slide 20: InfiniBand
InfiniBand is a high-performance switched fabric interface.
It is built upon a number (ranging from 1–12 or more) of highspeed, point-to-point and bidirectional serial links.
Maximum data throughput ranges from 2 Gigabits to 96 Gigabits for a 12X (12 bonded serial links) Quad Data Rate (QDR) configuration.
Linux support for InfiniBand comes thanks to Open Fabrics Alliance (OFA), an industry consortium created to address the lack of a standard InfiniBand API.

## Slide 21: GPIB
General-Purpose Interface Bus s still being used in engineering and scientific applications.
Many devices that are used for data acquisition and analysis are, in fact, equipped with a GPIB interface.
GPIB devices are connected together using a shielded cable that may have stackable connectors at both ends.
Linux support for GPIB is available thanks to the Linux GPIB kernel driver and library maintained

## Slide 22: I2C
Inter-Integrated Circuit (I2C) bus can be found in many embedded devices of all sizes and purposes.
I2C is a simple serial bus that enables the exchange of limited amounts of data among the IC components of an embedded system.
I2C can be implemented in both software and hardware.
Connecting devices using I2C requires only two wires, the serial clock line (SCL) with the clock signal and the serial data line (SDA) with the data.
All devices on an I2C bus are connected using the same wire pair.
The main kernel tree includes support for I2C, a number of devices that use I2C, and the related System Management Bus (SMBus).

## Slide 23: I/O
Input and output (I/O) are central to the role of any computerized device.
Linux supports a wide range of I/O devices.
Some of the I/O devices are supported in two forms by the kernel:
  by a native driver that handles the device’s direct connection to the system.
  through the USB layer to which the device may be attached.
There are, for instance, PS/2 keyboards and (older) parallel port printers along with USB keyboards and USB printers.

## Slide 24: Serial Port
The serial port is arguably every embedded system developer’s best friend.
Many embedded systems are developed and debugged using an RS232 serial link between the host and the target.
The simplicity of the RS232 interface has encouraged its widespread use and adoption.
Since RS232 is a hardware interface, the kernel doesn’t need to support RS232 itself, but Universal Asynchronous Receiver-Transmitter (UART).
The main serial (UART) driver in the kernel is drivers/char/serial.c.

## Slide 25: Parallel Port
The parallel port is seldom an important part of an embedded system.
One area of embedded systems development where the parallel port fits quite nicely, is simple multibit I/O.
When debugging, for instance, you can easily attach a set of LEDs to the parallel port’s pins.
Linux Device Drivers provides a more detailed description of how to use the parallel port as a simple I/O interface.

## Slide 26: Modem
Embedded systems that use a modem to call a data center are quite common.
Alarm systems, bank machines, and remote-monitoring hardware are all examples of embedded systems that need to communicate with a central system.
Since modems work in a wide variety of environments—including very remote locations that don’t have the latest cellular or computer networks—don’t count them out any time soon.
Modems in Linux are seen as serial ports.
They are accessible through the appropriate /dev serial device entry and are controlled by the same driver as the native serial UARTs.

## Slide 27: Data Acquisition
Data acquisition (DAQ) is at the basis of any process automation system.
Any scientific lab is filled with DAQ equipment linked.
The events occurring in the real world are measured by means of transducers.
There is no standard interface in Unix.
Comedi, the Linux control and measurement device interface, is the main package for interfacing with DAQ hardware.

## Slide 28: Keyboard
Most embedded systems are not equipped with keyboards.
Some may have a limited input interface.
Recent breeds of web-enabled and consumer-oriented embedded systems have some form of keyboard attached to them (Bluetooth keyboard)
Communication with the user in Linux is done by means of a terminal.
A keyboard is used for input and a console for output.
All keyboard input is considered by the kernel as input to a terminal.
Terminal input may involve many different layers of kernel drivers, but all keyboard input is eventually fed to the terminal I/O driver.

## Slide 29: Mouse
Embedded systems that have a user interface often offer some form of touch-based interaction.
In this sense, many embedded systems have a “mouse.”
The pointer device is seen on most Linux systems via the Input events layer located under /dev/input.
The device can be polled and read to obtain information regarding the pointer device’s movements and events.
Any programming that involves a pointer device would require an understanding of the protocol used by the device.
A number of libraries and environments already implement this level of decoding, and easy-to-use APIs are provided to obtain and react to pointer input.

## Slide 30: Display
Blinking lights, LEDs, and alphanumeric LCDs are the traditional visual apparel of embedded systems.
There is a push to replace such traditional display methods with visually rich interfaces.
In areas of embedded systems deployment, such as factory automation, avionics, PDAs, and Web Tablets.
With Linux there are many ways to control and program a display.
Some of these involve kernel support, but most rely mainly on code running in user space.
The most common way to provide a graphical interface with Linux is, of course, the X Window System (and others).
The X Window System provides only the basic graphical windowing environment.

## Slide 31: Sound
Consumer-oriented devices feature complex audio and video codec support—including MP3, Ogg Vorbis, AAC, MPEG, MPEG4, and H264.
With capability to multiplex multiple audio streams out to the same device simultaneously.
Unix, however, was never designed to accommodate sound.
Advanced Linux Sound Architecture (ALSA) is an example of a schemes that provides support for sound devices.
Various other projects provide sound servers: software that conceptually sits above the device interface and supports multiplexing, remote audio, and other fancy capabilities that aren’t really the domain of the sound device driver.